## Slide 1: Protecting the Accessible
Cryptography (crypto)/encryption protects information even when it is not under your physical control
Files, disks, network traffic
  At rest
  In transit
Also for identity
Protect keys
Why not encrypt everything fully?

## Slide 2: Chapter 10 Overview
Digital networking and reliable transmission
Building and operating a small-scale LAN
Reliability and error detection
Network protocols and the protocol stack
Network applications and resource sharing

## Slide 3: Potential Networking Risks
Physical theft of network hardware
Subversion of network switches or wiring
Disclosure – sniffing of sensitive messages
Forgery – constructing a bogus message
Masquerade – lying about the message source
Denial of service – make the net unusable

## Slide 4: An Example: Sharing a Printer
The Old Masonic building tenants share a LAN with a printer
Requirements
  All tenants shall contribute for utility bills and supplies
  All tenants shall have use of the shared network and printer
  Access shall only be granted to tenants

## Slide 5: Potential Controls
  Physical – isolate the net from attackers
  Mechanical – lock the building doors
  Logical – restrict network traffic to the suite
  Functional – provide no risky actions on the network
  Procedural – only suitemates have keys to the suite
  Cryptographic – use encryption to protect the network

## Slide 6: Physical Network Security

## Slide 7: Host and Network Integrity
Network worms
  Like the Morris worm, only up-to-date
  Use the latest Internet vulnerabilities
The botnet risk
  A botnet is a network of subverted computers
  Malware embeds special software
    Allows a botnet herder to operate the subverted computers (“bots”) remotely
    The bot software is hard to detect

## Slide 8: Transmitting Information
Message switching – send whole messages
  Sending and receiving are independent
  Recipient gets all of message or nothing
  Message size limits and longer delays
Circuit switching – connect two speakers
  Send and receive one or many messages
  Sender and recipient must both be available
Packet switching – send message in pieces
  More efficient, but requires complex endpoints

## Slide 9: Circuit Switching

## Slide 10: Packet Switching

## Slide 11: Packets Are Like Postcards
Easily carry short messages
Longer messages broken into segments
Recipient must reassemble the messages
Each message has a header that contains
  Destination address
  Damage detection, like a checksum
  Data to carry
  Sender's address: Optional and unreliable

## Slide 12: Transmitting Packets Reliably

## Slide 13: Packet Duplication

## Slide 14: Packet (“Frame”) Format

## Slide 15: Packet Contents
Source and destination “MAC” addresses
  Two-part address, unique across all networks
    3 bytes indicate the interface manufacturer
    3 bytes indicate specific interface
  All hosts hear all packets
    Hosts discard all packets not for them
Packet type – indicates the type of message it carries
CRC – an error detection code

## Slide 16: Finding a MAC Address
Keyboard commands
  Windows MSDOS: ipconfig
  Unix/Linix/Mac OS X: ifconfig
Graphical interface
  Windows: Via Network and Sharing Center
    “Details” under “Network Status”
  Mac OS: Via Network System Preferences
    “Ethernet tab” under the “Advanced” button

## Slide 17: Building a LAN/Ethernet
Most use twisted pair wire: Cat 5, 5+, or 6
Connections are from hosts to network “nodes” that pass the traffic between hosts
  A node “downlink” connects to a host
  A node “uplink” connects to other parts of the network
Two types of nodes in typical small LANs
  Hubs: broadcast to all hosts
  Switches: connects hosts pairwise, managable

## Slide 18: LAN Traffic
Physical Address – MAC
  frames sent on LAN (broadcast domain)
Ports – switch/hub ports
  table on switch (show mac address-table)
  mapped to MAC addresses
  sent out to all ports on hub

## Slide 19: LAN Traffic
IP Address – Virtual
  LAN addresses saved locally in ARP cache
      arp –a
  Packets sent to router port (gateway) to reach other LANs

## Slide 20: Network Protocol Software
We organize network software in layers
The layers form the protocol stack
Lower parts (network device drivers) may be in kernel mode
Higher parts are privileged OS programs
Highest parts are user application programs

## Slide 21: Protocol Stack

## Slide 22: A Simple, LAN-Oriented Stack
Top layer: Application layer
  An API is provided between the application programs and network software built into the OS
First layer below the API: Transport layer
  Links processes between hosts
Next layer: Link layer
  Builds packets to travel between hosts
Bottom layer: Device drivers/physical layer
  Actually transfers data to physical devices

## Slide 23: Layering Example: Ordering Pizza

## Slide 24: Packet Formats and Protocol Stacks

## Slide 25: Layers in a Simple LAN

## Slide 26: Network Applications: Client/Server