## Slide 1: Chapter 11 Outline
Network topology
Basic internet structure and routing
Internet host addressing
Network inspection tools

## Slide 2: Packet Types
Broadcast
Unicast
Multicast

## Slide 3: LAN
Broadcast domain
Physical (behind single router port)
Virtual (VLAN)
  Separate switch ports
  Virtual router ports

## Slide 4: Combining Computer Networks
Many early networks were Wide Area Networks or WANs
As LANs evolved, users wanted to connect LANs to WANs
Some connections had to span two or more WANs to reach from the desired source to the desired destination

## Slide 5: Internet Protocol Stack

## Slide 6: Routing Packets Between Networks
A node can move packets between LANs and/or WANs if it has a separate connection and MAC address on each network.
Every host connection also has a separate, unique Internet Protocol address (IP address)
Internet routing nodes (routers) use the IP address to direct the packet to its destination if on different network.

## Slide 7: IPv4 Address Format
Four Octets (eight bits, 2^8 power)
Dot decimal notation

## Slide 8: Early Internet Security
The Internet evolved from the ARPANET
  A research network developed by US DOD
  Relied on physical security, a restricted user community, and limited applications for security
As the community grew, security relied on host based authentication (passwords)
Internet Worm and Wily Hacker promoted the development of Internet firewalls
  Filtered traffic to try to block attacks

## Slide 9: Computing versus Telecom Networks
Computing
Internet protocol suite (TCP/IP) is the prevailing standard
Designed around packets
Focus on reliable data transmission between computers
Telecom
SS7 – Signalling System 7 – is the prevailing standard
Designed around circuits
Focus on telephone and cell phone voice service

## Slide 10: Evolution of Internet Structure

## Slide 11: Connections Between Hosts
Socket interface – a popular network API
  Provides basic send/receive functions
  Basic client/server functions
    Listen() – server awaits a connection
    Accept() – server accepts a connection
    Connect() – client requests a connection
Socket addresses – describe a process-to-process connection across the network

## Slide 12: Socket Address Format
Contains pair of IP addresses and port numbers
  Port number selects a client or server process
Sender Information
  Source port number – chosen randomly by client
  Source host's IP address
Recipient information
  Destination port number – preassigned for well known Internet services
  Destination host's IP address

## Slide 13: Examples: Well-Known Port Numbers
21 – FTP
22 – SSH
23 - Telnet
25 – SMTP
53 – DNS
80/443 – HTTP/S
389 – LDAP (AD)
3389 – Remote Desktop

## Slide 14: IP Packet Addressing

## Slide 15: IP Packet Format

## Slide 16: Address Resolution Protocol
“ARP” – looks up MAC or IP addresses on a LAN by asking other hosts for answers
  Uses Ethernet “broadcast” feature
  Asks “Who is 12.34.56.77?” for example
  The hosts with answers send responses
Hosts save answers in their ARP cache
  “arp” keyboard command prints the cache

## Slide 17: ARP Packet Format

## Slide 18: Routing and Addresses
Routing between hosts on a network may rely entirely on ARP
  Connections depend on host addresses
To send packets to other networks, routers look at the network address within an IP address
  The upper set of bits in the IP address represent the network address
  The network mask indicates which bits are network address bits

## Slide 19: Logical Subnets/LANs
Logical grouping of systems
Shared network portion of IP address
  /8 (CIDR) or 255.0.0.0 (Subnet mask)
  /16 or 255.255.0.0
  /24 or 255.255.255.0
Broadcast domain
Network address (i.e. 17.0.0.0/8)
Broadcast address (i.e. 17.255.255.255)
Router (gateway) required to send to other subnets – generally first address of subnet

## Slide 20: Internet Addresses in Practice
Dynamic/Static addresses
Private addressing
        10.0.0.0 - 10.255.255.255
        172.16.0.0 - 172.31.255.255
        192.168.0.0 - 192.168.255.255
  Only work on the internal network
  Must be converted to a public address to talk to Internet hosts on other networks
  Use Network Address Translation (NAT)

## Slide 21: Internet Addresses in Practice
Traditional IPv4 addresses are 32 bits long
  Accommodate a few billion hosts
  Public addresses are scarce
IPv6
  128 bits
  Not natively compatible with IPv4
  Faster (re-engineered packets)
  Security built-in

## Slide 22: Addressing and Scope

## Slide 23: Addressing Scope Example

## Slide 24: Network Inspection Tools
Wireshark
  Can monitor network traffic in real time
  Interprets frame and packet contents
  Recognizes standard Internet protocols
Network gateway – lists devices on the LAN
nmap
  Can “map” a network
  Scans the network address range to locate hosts and the open ports on each host
  Caution: May violate an ISP's use policy

## Slide 25: Wireshark Main Window
© Wireshark Foundation

## Slide 26: Wireshark: Ethernet Header
© Wireshark Foundation

## Slide 27: Wireshark: ARP Request
© Wireshark Foundation

## Slide 28: Wireshark: ARP Response
© Wireshark Foundation

## Slide 29: Wireshark: IP Header
© Wireshark Foundation

## Slide 30: Gateway List of Attached Devices
© Netgear

## Slide 31: nmap: Scan A Host’s Services